## Slide 1: Ran aware flow control tool
Jeremy Ostergaard

## Slide 2: What is RAFT?
Software tool to monitor radio channel conditions in a mobile LTE network
Enables use of statistics not available by standard in today’s wireless networks
Opens the door for more efficiently using flow control to manage networks

## Slide 3: Overview
Introduction to LTE
LTE Testbed at Hitachi
Introduction to RAFT
RAFT Functionality
Using RAFT for Flow Control
RAN Aware Video Optimization
Future of RAFT

## Slide 4: Introduction to LTE
Leading standard for 4G wireless in the United States
Two parts:
  evolved Universal Terrestrial Radio Access Network (E-UTRAN)
  Enhanced Packet Core (EPC)
Source: wirelesstech.info

## Slide 5: E-UTRAN
Handles the connection between UE’s (user equipment, e.g. a smartphone) and eNodeB’s (ENB, e.g. a cell tower)
Quality of connection is measured between an ENB and each UE connected to it
Channel Quality Indication determined based on this
  Decides what channel modulation method to be used
  Ranges from 0 to 15
  Higher- better signal, better bandwidth, higher efficiency
  Lower – worse signal, low bandwidth, higher chance of dropped message
Radio quality statistics stay in the E-UTRAN

## Slide 6: Flow Control in LTE
Policy and Charging Enforcement Function (PCEF) can set the flow control of traffic and UEs Decides what channel modulation method to be used
  Set Quality of Service (QoS) class
  Control minimum and maximum bandwidth
  Not really used in commercial LTE in the US
Takes into account congestion levels and number of UEs connected to divide bandwidth

## Slide 7: LTE Testbed (Core Network + RAN + Devices)
7
Testing UEs
Traffic
Generating
UES
RF-Combiner
eNB-1
eNB-2
eNB-3
EPC
PPRC Enforcer
File Server
Testbed Controller
USB Hub

## Slide 8: Previous Testbed Projects
Predictive and Preemptive Resource Controller
  Demonstrated at Hitachi CRL Kenpatsu October 2014
Predictive Video Optimization
Mobile Network on Twitter
  Demonstrated at MWC 2015

## Slide 9: RAFT Goals
Help prototype and gather data on LTE projects
What statistics to gather
  Radio Resource statistics available at ENB
  Subscriber IDs in EPC
How to gather them?
  JSON API
  Also available through command line interface
Central harvester server and multiple agent clients
What to do with them?
  Store in harvester
  Output to csv file and over API

## Slide 10: RAFT Agent
Configured through JSON Config File
Connects to Harvester through TCP
Connects to LTE Testbed through API
API requests to obtain UE metrics
  Metrics need to be merged
  Stored as JSON Object
Sends metrics as JSON to Harvester

## Slide 11: RAFT Harvester
Configured through JSON Config File
Opens TCP socket for clients
JSON API
  Takes UE statistics from agents
  Can take UE statistics from other Harvesters
  Will reply with UE data if sent a ‘get’ API request
Storing UE statistics
  Array of structures that hold the needed statistics
  Data on same UE from multiple agents is merged
  Statistics written to CSV file when updated

## Slide 12: Using RAFT For Flow Control
RAN Aware Flow Control utilizes UE statistics to improve efficiency
UEs running the same level of traffic use different amounts of radio resources
Using RAN statistics gathered from RAFT, flow control can be applied selectively based on radio conditions

## Slide 13: RAN Aware Video Optimization
RAN Aware Flow Control can be used to optimize adaptive video streams
Ideal starting quality can be determined by network with RAN statistics
Selective throttling in case of congestion:
  Reducing video quality of users farther away frees up proportionally more radio resources
  Freed Radio Resources can be used to improve the speed of others
  Additional Radio Resources may be given to users who have high spectral efficiency
  Improvement of the average QoE of the network

## Slide 14: The Future of RAFT
Hope to expand compatibility to other LTE networks
Network data Analytics
More statistic sources
  Gather RAN statistics at UE instead
  Network probing for statistics